## Slide 1: Inband Network Telemetry (INT) Version 2.0

## Slide 2: INT Ver 2.0 Functionality

## Slide 3: INT Header Types
Three types of INT Headers
  INT-MD: Hop-by-Hop - Intermediate devices (INT Transit Hops) must process this type of INT Header.
  INT MD: Destination - Destination headers must only be consumed by the INT Sink; intermediate devices must ignore Destination headers.
    To enable communication between INT Source and INT Sink.
    To deliver follow-up INT Packet to the INT Sinks
  INT-MX: Direct Export – Source devices, Intermediate devices (INT Transit Hops) and Sink devices must process this type of INT Header.

## Slide 4: INT-MD Functionality

## Slide 5: INT-MD Metadata Header and Metadata Stack Version 2.0
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: INT Metadata Header (Ver 2.0)
Ver (4b): INT Metadata header version. Should be 2 for this version.
Rep (2b): Replication Requested. Support is optional. Useful to explore all the valid physical forwarding paths (ECMP, LAG).
C (1b): Copy. If replication requested for data packets, the INT sink must be able to distinguish original packets from replicas.
E (1b): Max Hop Count Exceeded. This flag is set if a device cannot prepend its own metadata due to Remaining Hop Count reaching zero.
M (1b): MTU Exceed. This flag must be set if a device cannot add all of the requested metadata because doing so will cause the packet length to exceed egress link MTU.
R (10b): Reserved.
Hop ML (5b): Per-hop Metadata Length, the length of metadata in 4-Byte words to be inserted at each INT hop.
RemainingHopCnt (8b): The remaining number of hops that allowed to add their metadata to the packet.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: INT Metadata Header – Instruction Bitmap
INT instructions are encoded as a bitmap in the 16­ bit INT Instruction field: each bit corresponds to a specific standard metadata.
  bit0 (MSB): Switch ID
  bit1: Level 1 Ingress port ID (16 bits) + Egress Port ID (16 bits)
  bit2: Hop latency
  bit3: Queue ID (8 bits) + Queue occupancy (24 bits)
  bit4: Ingress timestamp
  bit5: Egress timestamp
  bit6: Level 2 Ingress port ID (32 bits) + Egress Port ID (32 bits)
  bit7: Egress port TX utilization
  Bit8: Buffer Occupancy (32 bits)
  Bit 14: Domain Specific Instruction
  bit15: Checksum Complement
  The remaining bits are reserved
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: INT Metadata Header – Instruction Bitmap
Domain Specific ID (16b): Domain Specific ID, the unique ID of the INT Domain.
DS Flags (16b): Flags relevant to the INT domain identified by the Domain Specific ID.
DS Instruction (16b): Instruction bit map specific to the INT domain identified by the Domain Specific ID.
Domain Specific INT instructions are encoded as a bitmap in the 16­ bit DS Instruction field: each bit corresponds to a specific domain specific metadata.
  bit0 (MSB): Aggregated Metadata
  bit1: Threshold Exceeded
  The remaining bits are reserved
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 9: INT Instruction Handling
Each INT Transit device adds its own metadata values as specified in Instruction Bitmap. If the Domain Specific ID doesn’t match any of its configured Domains Specific ID(s), then ignore the Domain Specific Instructions.
  Each instruction metadata is 4 bytes.
  Metadata size = Instruction Count * 4 bytes.
  Metadata prepended at the top of the Metadata Stack.
  If unable to provide metadata specified in instruction bitmap, indicate invalid metadata (reserved value 0xFFFF_FFFF).
  If Metadata size cannot be prepended, skip INT handling.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ver |Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 10: INT Domain Specific Instruction Handling
Each INT Transit device adds its own metadata values as specified in Domain Specific Instruction Bitmap if Domain Specific ID matches one of its configured Device Specific ID(s).
  Each instruction metadata is 4 bytes.
  Metadata size = Instruction Count * 4 bytes.
  Metadata prepended at the top of the Metadata Stack.
  If unable to provide metadata specified in instruction bitmap, indicate invalid metadata (reserved value 0xFFFF_FFFF).
  If Metadata size cannot be prepended, skip INT handling.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ver |Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| INT Metadata Stack (Each hop inserts HOP ML * 4B of metadata) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . . . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Last INT Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: INT-MX Functionality

## Slide 12: INT-MX Metadata Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 13: INT-MX Metadata Header
Ver (4b): INT Metadata header version. Should be 2 for this version.
Rep (2b): Replication Requested. Support is optional. Useful to explore all the valid physical forwarding paths (ECMP, LAG).
C (1b): Copy. If replication requested for data packets, the INT sink must be able to distinguish original packets from replicas.
E (1b): Max Hop Count Exceeded. This flag is set if a device cannot prepend its own metadata due to Remaining Hop Count reaching zero.
M (1b): MTU Exceed. This flag must be set if a device cannot add all of the requested metadata because doing so will cause the packet length to exceed egress link MTU.
R (10b): Reserved.
Hop ML (5b): Per-hop Metadata Length, the length of metadata in 4-Byte words to be inserted at each INT hop.
RemainingHopCnt (8b): The remaining number of hops that allowed to add their metadata to the packet.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 14: INT-MX Metadata Header – Instruction Bitmap
INT instructions are encoded as a bitmap in the 16­ bit INT Instruction field: each bit corresponds to a specific standard metadata.
  bit0 (MSB): Switch ID
  bit1: Level 1 Ingress port ID (16 bits) + Egress Port ID (16 bits)
  bit2: Hop latency
  bit3: Queue ID (8 bits) + Queue occupancy (24 bits)
  bit4: Ingress timestamp
  bit5: Egress timestamp
  bit6: Level 2 Ingress port ID (32 bits) + Egress Port ID (32 bits)
  bit7: Egress port TX utilization
  Bit8: Buffer Occupancy (32 bits)
  Bit 14: Domain Specific Instruction
  bit15: Checksum Complement
  The remaining bits are reserved
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 15: INT-MX Metadata Header – Instruction Bitmap
Domain Specific ID (16b): Domain Specific ID, the unique ID of the INT Domain.
DS Instruction (16b): Instruction bit map specific to the INT domain identified by the Domain Specific ID.
DS Flags (16b): Flags relevant to the INT domain identified by the Domain Specific ID.
Domain Specific INT instructions are encoded as a bitmap in the 16­ bit DS Instruction field: each bit corresponds to a specific domain specific metadata.
  bit0 (MSB): Aggregated Metadata
  bit1: Threshold Exceeded
  The remaining bits are reserved
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Rep|C|E|M| Reserved | Hop ML |RemainingHop Cnt |
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instruction Bitmap | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DS Instruction | DS Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 16: INT Transport Options - INT in IPv4 (GRE)

## Slide 17: INT in IPv4 (GRE)
GRE encapsulation is defined in [RFC2784].
The GRE Protocol Type value is TBD_INT.
The INT Header is defined as follows:
  INT Type: 8-bit field defining the INT Header type, as defined in
    INT-MD: Hop-By-Hop Type
    INT-MD: Destination Type
    INT-MX: Direct Export
  INT Hdr Len: 8-bit Length field contains the length of the variable INT data octets in 4-octet units.
  Next Protocol: 16 bits Next Protocol Type field contains the protocol type of the packet following INT protocol header. When the most significant octet is 0x00, the Protocol Type is taken to be an IP Protocol Number as defined in [IP_PROT]. Otherwise, the Protocol Type is defined to be an EtherType value from [ETYPES]. An implementation receiving a packet containing a Protocol Type which is not listed in one of those registries SHOULD discard the packet.

## Slide 18: INT in IPv4 (GRE)
Structure of GRE Encapsulated Packet:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Delivery Header |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| GRE Header |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Payload Packet |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 19: INT in IPv4 (GRE) – Delivery Header
Outer Ethernet Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| (Outer) Desitnation MAC Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|(Outer)Destination MAC Address | (Outer) Source MAC Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| (Outer) Source MAC Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Optional Ethertype=C-Tag 802.1Q| Outer VLAN Tag Information |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ethertype 0x800 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Outer IPv4 Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| HL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol 0x2F | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| (Outer) Source Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| (Outer) Destination Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 20: INT in IPv4 (GRE) – GRE Header
GRE Header:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|C|R|K|S|s|Recur| Flags | Ver | Protocol Type = TBD_INT | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Checksum (optional) | Offset (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ G
| Key (Optional) | R
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ E
| Sequence Number (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Routing (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| INT Type | INT HDR Len | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | N
| Variable Option Data (INT Metadata Headers and Metadata] | T
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
When the INT data fields are included within an encapsulation that identifies the next protocol using an EtherType (e.g., GRE or Geneve) the presence of INT data fields are identified with TBD_INT. When this EtherType is used, an additional INT header is also included. This header indicates the type of INT data that follows, and the next protocol that follows the INT data.

## Slide 21: INT- MD (Ver 2.0) in IPv4 (GRE)
GRE Header:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|C|R|K|S|s|Recur| Flags | Ver | Protocol Type = TBD_INT | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Checksum (optional) | Offset (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ G
| Key (Optional) | R
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ E
| Sequence Number (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Routing (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| INT Type | INT HDR Len | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| INT-Type - MD | Reserved | Length | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-| |
|Ver = 2|Rep|C|E|M| Reserved | Hop ML | RemainingHop Cnt | I
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ N
| Instruction Bitmap | Domain Specific ID | T
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| DS Flags | DS Instruction | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Variable Option Data (INT Metadata Metadata] | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| Payload Original Packet |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 22: INT- MX (Ver 2.0) in IPv4 (GRE)
GRE Header:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|C|R|K|S|s|Recur| Flags | Ver | Protocol Type = TBD_INT | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Checksum (optional) | Offset (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ G
| Key (Optional) | R
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ E
| Sequence Number (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Routing (Optional) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| INT Type | INT HDR Len | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| INT-Type - MX | Reserved | Length | Next Protocol | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-| |
|Ver = 2|Rep|C|E|M| Reserved | Hop ML | RemainingHop Cnt | I
​+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ N
| Instruction Bitmap | Domain Specific ID | T
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| DS Flags | DS Instruction | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| Payload Original Packet |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 23: INT - Telemetry Report Export

## Slide 24: Telemetry Report
INT Sink Nodes exports to telemetry monitoring systems.
Generated for three categories:
  Tracked Flows
  Dropped Packets
  Congested Queues
A report associated with one or more categories.
Events trigger telemetry reports
Modes :
  Direct Export – INT-MX
  In-band Mode – INT-MD

## Slide 25: Telemetry Report – INT-MD Mode
Tracked Flows
  Generated for all packets of a flow matching a ACL/Profile Table entry and configured to perform the sink functionality.
Dropped Packets
  Generated for all dropped packets of a flow matching a ACL/Profile Table entry.
  This provides visibility into the impact of packet drops on user traffic.
Congested Queues
  Generated for traffic entering a specific queue during a period of queue congestion.
  This provides visibility into the traffic causing and prolonging queue congestion
  Enables the detection and “re-play” of a short microburst
The reports include the metadata stack received in the packet and the local switch metadata.
The reports shall include the original packet header for collector to be able correlate various reports.

## Slide 26: Telemetry Report – INT-MX Mode
Tracked Flows
  Generated for all packets of a flow matching a ACL/Profile Table entry and configured to perform the postcard functionality.
Dropped Packets
  Generated for all dropped packets of a flow matching a ACL/Profile Table entry.
  This provides visibility into the impact of packet drops on user traffic.
Congested Queues
  Generated for traffic entering a specific queue during a period of queue congestion.
  This provides visibility into the traffic causing and prolonging queue congestion
  Enables the detection and “re-play” of a short microburst
The reports include local switch metadata only.
The reports shall include the original packet header for collector to be able correlate various reports.

## Slide 27: Transport of Telemetry Reports
UDP Encapsulation
Any outer encapsulation, not specified and user defined.
Source Port is optional. May be used to carry flow entropy (hash of the inner 5-tuple). Otherwise, it should be set to 0.
Destination Port is user configurable. Same destination port value for all telemetry reports in a deployment.
Telemetry Report UDP Header (8 octets)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Port | Destination Port |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 28: Telemetry Report Header – Ver 2.0
Telemetry Report Header (16+ Octets)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Length |NProt| RepMdBits |Reserved |D|Q|F| hw_id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Switch ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ingress Timestamp |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Variable Optional Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Nprot | Extension Length | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extensions Data |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extensions Data | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Length: Indicates length of report header in multiple of 4 octets, including the optional metadata.
Nproto: Next Protocol
  0 – Ethernet
  1 – IPv4
  2 – IPv6
  3 – Telemtery Extensions
RepMdBits: Report Metadata Bits (each bit represents 4 octets of optional metadata)
  0 – Ingress ID (16 bits) & Egress Port ID (16 bits)
  1 – Hop Latency
  2 – Queue ID (8 bits) + Queue Occupancy (24 bits)
  3 – Egress Timestamp (32 bits)
  4 – Queue ID (8 bits) + Drop Reason (8 bits) + Padding (16 bits)
  5 – Egress Port TX Utilization
  6 – Buffer ID (8 bits) + Buffer Occupancy (24 bits)
  7 - Level 2 Ingress port ID (32 bits) + Egress Port ID (32 bits)
D – Dropped – Indicates at least one packet was dropped.
Q – Congested Queue
F – Tracked Flow Association - indicated report is for a tracked flow.
hw_id: Hardware sub-system within the source that generated this report
Switch ID: The unique ID of a switch (administratively assigned).
Sequence Number: Reflects the sequence of reports from a specific hw_id
Ingress Timestamp: Device local time when packet was first received on the ingress physical or logical port, in nanoseconds

## Slide 29: Telemetry Report Header – Ver 2.0 (contd.)
Telemetry Report Header (16+ Octets)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ver = 2|Length |NProt| RepMdBits |Reserved |D|Q|F| hw_id |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Switch ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ingress Timestamp |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Variable Optional Metadata |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Nprot | Extension Length | Domain Specific ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extensions Data |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extensions Data | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| . | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Length: Indicates length of report header in multiple of 4 octets, including the optional metadata.Extensiop
Nproto: Next Protocol
  0 – Ethernet
  1 – IPv4
  2 – IPv6
  3 – Telemtery Extension

## Slide 30: Correlation of Telemetry Report
Monitoring Systems based upon:
  Original Packet headers.
  Association Bit for each category.