## Slide 1: INT with UDF
P4 working group
September 6, 2018

## Slide 2: User Defined Fields (UDF)
Some switches and routers allow users to specify arbitrary user defined fields using a base / offset / length definition
  Fields can be used as match criteria, e.g. in ACLs
  Fields can be used as part of ECMP / LAG hash to better distribute traffic load across the network
Ethernet
IP
TCP
Payload
offset
UDF

## Slide 3: INT Impact on UDF
If using cut through switching, finding UDF field after parsing INT stack is too late
What is the base? INT stack?
Ethernet
IP
TCP
Payload
offset?
UDF
Variable-Length INT stack
INT

## Slide 4: Proposal: Add UDF / Flow Field Before INT Stack
Source copies UDF into INT UDF / Flow field, precedes the INT stack
Transit (and sink) switches use INT UDF field for ECMP / LAG hash
Ethernet
IP
TCP
Payload
UDF
Variable-Length INT stack
INT
INT UDF / Flow Field
Ethernet
IP
TCP
Payload
offset
UDF

## Slide 5: Where to Put UDF / Flow Field?
INT UDF / Flow field is only needed in non-tunnel encaps such as INT over TCP / UDP
  For tunnel encaps, UDF can be included when determining value of entropy field (e.g. outer UDP source port)
INT shim header?
INT hop-by-hop metadata header?